Sedimentary Records of Contaminant Inputs in Frobisher Bay, Nunavut (2017-2018)
Data Dictionary

Description of the database

This dataset includes geochemical and contaminant data measured in surface sediments and sections of sediment cores collected from Koojesse Inlet and other locations in Frobisher Bay, Nunavut. Sediment cores and surface sediment were collected throughout Koojesse Inlet in 2017 by the Canada-Nunavut Geoscience Office aboard MV Nuliajuk vessel. Sediment cores were collected from inner and outer Frobisher Bay in 2018 by University of Manitoba researchers onboard the CCGS Amundsen icebreaker.

Geochemical parameters measured in sediment core samples included radioisotopes (210Pb and 137Cs), carbon and nitrogen content, and stable isotopes (δ13C and δ15N). Contaminants measured in selected sediment sections included total mercury (THg), major and trace elements, polychlorinated biphenyls (PCBs), polycyclic aromatic hydrocarbons (PAHs), and per and polyfluoroalkyl substances (PFASs).

Region studied

Samples were collected from inner Frobisher Bay near the City of Iqaluit and outer Frobisher Bay in Nunavut, Canada.

Figure 1. Maps of the sampling sites in Frobisher Bay where sediment cores were collected.

Description of data collection

Sampling

Sediment samples were collected from 20 sites in Koojesse Inlet, Frobisher Bay, in 2017. In 2018, two additional cores were collected, one along the central axis of inner Frobisher Bay (core Bell_10) and one in outer Frobisher Bay (core 12C). Seven sediment cores from 2017 and 2018 were selected for contaminant analysis. The cores from Koojesse Inlet were collected from Research Vessel (RV) Nuliajuk in 2017 using an Ocean Instruments 25 × 25 × 50 cm GMX-25 GOMEX box corer. In 2018, cores Bell_10 and 12C were collected from CCGS Amundsen using an Ocean Instruments 50 × 50 × 50 cm BX-650 MK-III box corer. Sediment cores were sub-sectioned in 1 or 2-cm intervals throughout the length of each core.

Once retrieved, cores from both types of box corers were subsampled by inserting a 10 cm diameter tube into the sediment, capping at both ends, and removing the push core from the box core. The cores were extruded and sectioned into 1 cm lengths for the first 5 cm and 1-2 cm lengths for the remaining length of the core. Each section was homogenized and stored in trace-clean, 250 mL, amber, wide-mouth jars for organic geochemistry analyses, and plastic bottles for nonorganic geochemistry analyses. Sediment samples were frozen at –20 °C and shipped to the Centre for Earth Observation Science (CEOS) at the University of Manitoba in Winnipeg, MB, for further processing. Samples were thawed, rehomogenized, subsampled, weighed to determine wet weight and frozen, then freeze dried at -55 °C for ~96 hours. Subsamples were reweighed to determine dry weight then ground with a pestle and mortar. Sediment porosity was calculated using the difference between wet and dry weights and corrected for salt content.

Radioisotopes

Downcore activities of 210Pb (lead), 226Ra (radium), and 137Cs (cesium) were indirectly measured in cores 4, 8, and 16 by the alpha-counting method at Flett Research Ltd. Approximately 0.5 g of dry sample was spiked with a 209Po-yield (polonium) tracer and digested in hot nitric acid, dried and made up in 1.5 N hydrochloric acid (HCl). 210Po and 209Po alpha-emitting isotopes were plated out on silver planchets. The activity of polonium isotopes was determined by alpha-particle spectrometry.

Gamma emissions of 210Pb, 226Ra, and 137Cs were measured in cores 14, 15, Bell_10, and 12C at the Environmental Radiochemistry Laboratory (ERL) at the University of Manitoba, Winnipeg, MB. Cores 4, 8, and 16 were also analyzed for 137Cs at ERL. Dried and ground samples were weighed and sealed in 50 by 9 mm Petri dishes for 21 days. Samples were measured for total 210Pb and 137Cs by counting gamma emissions at 46.5 and 661 kiloelectronvolts (keV), respectively. 214Pb, the granddaughter isotope of 226Ra, was counted at 352 keV to estimate 226Ra activities. Activities were counted for 12-24 hours on Canberra Industries, Inc. Broad Energy Geranium detectors.

### Carbon and nitrogen content
At the University of British Columbia, total carbon and nitrogen (TC and TN), total inorganic carbon (TIC), total organic carbon (TOC), stable carbon (δ13C), and nitrogen (δ15N) isotope compositions were measured. Total carbon and nitrogen (TC and TN) measurements were performed using a Elementar Americas elemental analyzer. Total inorganic carbon (TIC) was determined by CO2 coulometer, and then organic carbon (TOC) obtained by difference. Stable carbon (d13C) and nitrogen (d15N) isotope composition was determined by an in-line isotope ratio mass spectrometer, following pre-treatment of the d13C subsample with 10% HCl to remove inorganic carbon.

Major and trace elements

Sediment subsamples were analyzed for major and trace elements at Institut national de la recherche scientifique (INRS) laboratories, Quebec City, QC, following US EPA Method 200.7 and US EPA Method 200.8. Before analysis, ~0.1 g of sample was digested by adding 4 mL nitric acid (HNO3) and heating at 100 C until dry. After cooling, 1.6 mL HCl was added. The sample was then heated for 1-2 hours at 100 C, cooled, and digested over night with the addition of 2 mL hydrogen fluoride (HF). The next day, samples were heated to 150 C. 15 mL HNO3 was added, and the samples were left at room temperature for two weeks and then sent for analysis at Institut national de la recherche scientifique (INRS) laboratories. Major elements aluminum (Al), iron (Fe), manganese (Mn), and phosphorus (P) were analyzed by inductively coupled plasma-atomic emission spectrometry (ICP-AES) according to US EPA Method 200.7. Trace elements and isotopes arsenic (As), copper (Cu), molybdenum (Mo), lead (Pb), retene (187Re), zinc (Zn), and uranium (238U) were analyzed by inductively coupled plasma – mass spectrometry (ICP-MS) according to US EPA Method 200.8.

Total mercury (THg)

THg was measured at the Centre for Earth Observation Science (CEOS) laboratory in Winnipeg, MB, according to US EPA Method 7473. THg was measured on ~50 mg of predried and ground sediment using a Teledyne Leeman Labs Hydra II AA direct mercury analyzer, according to US EPA Method 7473. Calibration was performed prior to analysis. Three certified reference materials (MESS-3, NIST 2709a, and PACS-3) were run to validate the curve at the beginning of the analysis. During analysis, each batch included 10 samples with one duplicate, MESS-3 and NIST 2709a certified reference materials, and one blank.

Polycyclic aromatic hydrocarbons (PAHs)

Sediment samples were analyzed for 15 PAHs at the Petroleum Environmental Research Laboratory at CEOS in Winnipeg, MB, following US EPA Method 3630C. A mixture of acetone and hexane was added to the predried and ground samples. After addition of internal standard to the samples, blanks, and a quality control sample, the samples underwent microwave extraction following US EPA Method 3546 using a CEM Mars 6 Microwave Oven Vessel. Sulfur was removed from the sediments according to US EPA Method 3660B, followed by silica column chromatography following US EPA Method 3630C using a 250 mm long x 10 mm ID column. Samples were then injected into an Agilent 7890 GC/7010b QQQ for analysis. Internal standard was added to the samples, blanks, and a quality control (NIST) sample.

Polychlorinated biphenyls (PCBs)

Samples were analyzed for 162 individual or co-eluting PCB congeners at the ALS Global Labs in Burlington, ON, according to US EPA Method 1668C. Sediment samples were Dean-Stark Soxhlet extracted using toluene as the solvent. Instrumental analysis was via gas chromatograpy/high resolution mass spectrometry (GC-HRMS) isotope dilution on an SPB Octyl 30m 0.25 bore and 0.25 film thickness column and using helium as carrier gas on a Waters Premier Autospec, following US EPA Method 1668C. Samples were analyzed in batches with a blank and control sample. Isotopically labeled surrogate standards were added to each sample to assess recovery.

Per and polyfluoroalkyl substances (PFASs)

Samples were analyzed for 26 PFASs at the Environment and Climate Change Canada lab in Burlington, ON, using previously reported methods based on the addition of stable isotopes, solvent extraction with carbon clean-up and analysis by liquid chromatography tandem mass spectrometry. An internal standard mixture of isotopically labeled PFASs and methanol was added to dried subsamples. Samples were vortexed, ultrasonicated, shaken on a table shaker, and centrifuged. A second aliquot of methanol was added, sonicated, shaken, and centrifuged. The extract was evaporated using a gentle stream of nitrogen to 1 ml. The samples were transferred to a centrifuge tube containing carbon and glacial acetic acid and centrifuged. The extract was decanted to a vial, concentrated then combined with an instrument performance standard (methanolic cocktail of isotopically labeled PFAS surrogates). Ammonium acetate in polished HPLC-grade water was added. The HPLC-grade water was polished to remove PFASs using an OASIS WAX solid phase extraction cartridge. The extracts were then analyzed by liquid chromatography tandem mass spectrometry (LC-MS/MS). The LC was an Acquity i-class (Waters), with a Acquity C18 column BEH (2.1x100 mm, 1.7 μm), and the mass spectrometer was a Waters Xevo TQS. For each batch of samples, 3 method blanks were performed, one samples was spiked before extraction, and one sample was spiked after extraction to calculate percent recovery. Analytes were quantified using a 16-level calibration curve. One sample was extracted and analyzed in triplicate and based on 9 PFAS analytes that were above detection limits.

Data

All data provided are raw except for duplicate data which has been averaged, and is reported in dry weight. Values preceded with a “<” indicate that concentration was below the limit of detection (LOD). The PFAS data provided is also blank and recovery corrected.

Table 1. Definitions of the variables used in the dataset.
Variable name	Definition
Physical properties
MeasurementID	Unique identifier for measurement data
CoreID	Name of sediment core
alternate_coreID	Alternative/second name for sediment core
Year	Year that the core was sampled
Date
MinSlice_cm	Minimum depth of the slice in the sediment core (centimeters)
MaxSlice_cm	Maximum depth of the slice in the sediment core (centimeters)
latitude	Geographic latitude (positive values are north of the equator, negative values are south of it)
longitude	Geographic longitude (positive values are east of the Greenwich Meridian, negative values are west of it)
measurement_remark	Comment on the minimum and maximum depth of the slices taken from the cores (centimeters)
water_depth_m	Depth of the water where the core was collected (meters)
Porosity	Porosity value for the sediment slice
Geochemistry
total_Hg_ng/g	Total mercury (THg, nanograms per gram)
total_N	Total nitrogen
total_C	Total carbon (organic and inorganic)
organic_C	Total organic carbon (%)
d15N	δ15N
d13Corg	δ13C (‰)
Al_mg/kg	Aluminum (milligrams per kilogram)
As_mg/kg	Arsenic (milligrams per kilogram)
Cu_mg/kg	Copper (milligrams per kilogram)
Fe_mg/kg	Iron (milligrams per kilogram)
Mn_mg/kg	Manganese (milligrams per kilogram)
Mo_mg/kg	Molybdenum (milligrams per kilogram)
P_mg/kg	Phosphorus (milligrams per kilogram)
Pb_mg/kg	Lead (milligrams per kilogram)
Zn_mg/kg	Zinc (milligrams per kilogram)
187Re	187Retene (milligrams per kilogram)
238U	238Uranium (milligrams per kilogram)
Polycyclic aromatic hydrocarbons (PAHs)
Anthracene_ng/g	Anthracene (nanograms per gram)
Pyrene_ng/g	Pyrene (nanograms per gram)
Benz_a_anthracene_ng/g	Benz[a]anthracene (nanograms per gram)
Naphthalene_ng/g	Naphthalene (nanograms per gram)
Benzo_k_fluoranthene_ng/g	Benzo[k]fluoranthene (nanograms per gram)
Benzo_a_pyrene_ng/g	Benzo[a]pyrene (nanograms per gram)
Benzo_g_h_i_perylene_ng/g	Benzo[g,h,i]perylene (nanograms per gram)
Acenaphthene_ng/g	Acenaphthene (nanograms per gram)
Fluorene_ng/g	Fluorene (nanograms per gram)
Phenanthrene_ng/g	Phenanthrene (nanograms per gram)
Fluoranthene_ng/g	Fluoranthene (nanograms per gram)
Chrysene_ng/g	Chrysene (nanograms per gram)
Benzo_b_fluoranthene_ng/g	Benzo[b]fluoranthene (nanograms per gram)
Dibenz_a_h_anthracene_ng/g	Dibenz[a,h]anthracene (nanograms per gram)
Indeno_1_2_3_c_d_pyrene_ng/g	Indeno[1,2,3-c,d]pyrene (nanograms per gram)
Polychlorinated biphenyls (PCBs)
PCB-001_pg/g – PCB-209_pg/g	Individual or co-eluting polychlorinated biphenyl congener (picograms per gram). Co-eluting congeners are separated with a slash symbol (/).
Per and polyfluoroalkyl substances (PFASs)
PFBA_ng/g	Perfluorobutanoic acid (PFBA, nanograms per gram)
PFPeA_ng/g	Perfluoropentanoic acid (PFPeA, nanograms per gram)
PFHxA_ng/g	Perfluorohexanoic acid (PFHxA, nanograms per gram)
PFHpA_ng/g	Perfluoroheptanoic acid (PFHpA, nanograms per gram)
PFOA_ng/g	Perfluorooctanoic acid (PFOA, nanograms per gram)
PFNA_ng/g	Perfluorononanoic acid (PFNA, nanograms per gram)
PFDA_ng/g	Perfluorodecanoic acid (PFDA, nanograms per gram)
PFUnDA_ng/g	Perfluoroundecanoic acid (PFUnDA, nanograms per gram)
PFDoDA_ng/g	Perfluorododecanoic acid (PFDoDA, nanograms per gram)
PFTriDA _ng/g	Perfluorotridecanoic acid (PFTriDA, nanograms per gram)
PFTeDA_ng/g	Perfluorotetradecanoic acid (PFTeDA, nanograms per gram)
PFHxDA_ng/g	Perfluorohexadecanoic acid (PFHxDA, nanograms per gram)
PFOS_ng/g	Perfluorooctanesulfonate (PFOS, nanograms per gram)
PFDS_ng/g	Perfluorodecanesulfonate (PFDS, nanograms per gram)
PFECHS_ng/g	Perfluoroethylcyclohexane sulfonate (PFECHS, nanograms per gram)
PFHxS_ng/g	Perfluorohexanesulfonate (PFHxS, nanograms per gram)
PFBS_ng/g	Perfluorobutanesulfonate (PFBS, nanograms per gram)
FOSA_ng/g	Perfluorooctane sulfonamide (FOSA, nanograms per gram)
HFPO_ng/g	Tetrafluoro-2-(heptafluoropropoxy)propanoate (HFPO, nanograms per gram)
ADONA_ng/g	4,8-dioxa-3H-perfluorononanoate (ADONA, nanograms per gram)
8ClPFOS _ng/g	8-chloroperfluoro-1-octanesulfonate (8ClPFOS, nanograms per gram)
9Cl-PFONS_ng/g	9-chlorohexadecafluoro-3-oxanonane-1-sulfonate (9Cl-PFONS, nanograms per gram)
11-PFONS_ng/g	11-chloroeicosa fluoro-3-oxaundecane-1 sulfonate (11-PFONS, nanograms per gram)
5_3_FTCA_ng/g	5:3 fluorotelomer acid (5 3 FTCA, nanograms per gram)
7_3_FTCA_ng/g	7:3 fluorotelomer acid (7 3 FTCA, nanograms per gram)
8_3_FTCA_ng/g	8:3 fluorotelomer acid (8 3 FTCA, nanograms per gram)